## Slide 1: Charge Manipulation of Flow in Nanochannels
Thomas Prevenslik
QED Radiations
Berlin, Germany and Discovery Bay, Hong Kong
1
Notes: Enter speaker notes here.

## Slide 2: Introduction
Water flow through nanochannels is found to be 2-5 orders-of-magnitude greater than predicted by the no-slip Hagen-Poiseuille equation of classical physics.
, b is the slip length
But slip lengths of 50 microns are required to reproduce the flow in 7 nm channels. Since the water/graphene slip length is on the order of 50 nm, the required slip-length is 1000 times larger than that of non-wetting boundaries.
Classical physics is not applicable
2

## Slide 3: Background
3
In 2015, flow enhancement in nanochannels was shown [1] by QM to produce charge causing friction to vanish that does not occur in classical physics
QM = quantum mechanics
Recent developments:
MD shows charge outside nanochannel [2] stops flow.
MD [3] shows that a vibrational charge increases flow by breaking hydrogen bonds with the channel wall.
Purpose: Review and Comment
[1] Prevenslik T., The Bernoulli Equation in nanochannels, Topical Problems in Fluid Mechanics, 2015.
[2] J. Li, et al., Electrostatic gating of a nanometer water channel, Proc. Natl. Acad. Sci. USA,104, 3687, 2007.
[3] Kou, J. et al., “Electromanipulating Water Flow in Nanochannels,” Angew. Chem. vol. 127: pp. 2381, 2015.

## Slide 4: QM v. Classical Physics
4
Heat Capacity of the Atom
TIR Confinement
EM Confinement
Simple QED
Charging
CNT/Membrane Pore
X-ray Radiation

## Slide 5
Heat Capacity of the Atom
Chart: EM Wavelength - l - microns
| 0.5 | 1 | 5 | 10 | 15 | 30 | 50 | 100 | 200 | 500 | 1000
 | 5.0957e-42 | 1.7789e-21 | 1.6842e-05 | 0.0010311 | 0.0035198 | 0.010475 | 0.015415 | 0.020163 | 0.022897 | 0.024656 | 0.025262
5
Nanochannels
kT
Macrochannels
QM
Vanishing heat capacity  EM confinement must be submicron
Classical Physics

## Slide 6: TIR Confinement
At Topical Problems in Fluids 2015, I argued the confinement of photons by TIR in the surface of a body if its refractive index is greater than that of the surroundings.
TIR = total internal reflection
UPDATE: TIR confinement not significant Fluid molecules that enter the nanochannels are placed under EM confinement.
f = ( c/n ) /   = 2 d E = h f
E = Planck energy
h = Planck’s constant
d = channel height
n = Refractive index of fluid
6

## Slide 7: EM Confinement
7
EM confinement of atoms at the nanoscale is a natural consequence of high S/V ratios
S/V = surface-to-volume
Almost all of the heat absorbed in a nanostructure is therefore deposited in its surface
Atoms are momentarily placed under high EM confinement.
Since nanostructures are submicron, the EM confinement is submicron and the heat capacity vanishes.
Heat cannot be conserved by temperature !
How is heat conserved?

## Slide 8: Simple QED
8
Simple QED is proposed to conserve heat
QED = quantum electrodynamics
But far simpler than Feynman’s QED !
Briefly stated:
Under the QM restriction that the heat capacity of the atom vanishes, the heat Q absorbed in the nanostructure surface creates standing EM radiation having half wavelength /2 = d, where d is the minimum dimension of the nanostructure
Heat
Q
Standing Wave
/2 = d
Nanochannel
d

## Slide 9: Charging Mechanisms
CNT in water
Pore in Biological Membrane
9

## Slide 10: CNT
Q
Standing X-ray
/2 = d
Nanochannel
d
Water
Molecules
kT
10
For CNTs having diameters d  0.84 nm in water with index n  1.30, the EM radiation at X-ray levels has wavelength  = 2nd = 2.18 nm with Planck energy E = hc/ = 0.57 keV.
X-ray photon energy E = 3NU, where N is the number of water molecules. For E = 570 eV and U =1.5 kT, N = 4895.
In a cylindrical slice of width S in a diameter D through the CNT is , N = (D/S)2/4 gives D  25 nm.
Charging requires turbulence to renew heat Q continuously.
Turbulence

## Slide 11: Membrane Pore
Q
Standing X-ray
/2 = d
Nanochannel
d
Membrane
For X-ray levels in pores of membranes, the radius R2 is the boundary where kT > 0.
Heat Q flows into nanochannel. The prior QM plot of heat capacity shows R2 = 50 to 100 microns at ambient temperature T = 300 K
kT limit Radius
R2
11

## Slide 12: Membrane Pore
R2 = 50 micron
R2 = 100 micron
12
The X-ray creation time  for 570 eV X-rays.
R2 = boundary where kT > 0, R2 = 50,100 microns
L = thickness of membrane, L = 50 microns.
K = thermal conductivity, K = 0.5 W/m-K
T = temperature, T = 300 K
Heat Q flows into nanochannel at  < 10 fs which is sufficiently instantaneous to assure the X-ray transition and charging
Chart: 
| 1 | 2 | 5 | 10 | 20 | 50 | 100
 | 9.094 | 8.5114 | 7.7413 | 7.1587 | 6.5761 | 5.806 | 5.2234
 | 9.6766 | 9.094 | 8.3239 | 7.7413 | 7.1587 | 6.3885 | 5.806

## Slide 13: MD Simulations
Programs
Model-Method
Results
13

## Slide 14: Programs
MD computer programs, e.g., LAMMPS based on classical physics that allow the atom the heat capacity to change in temperature are invalid by QM.
In the literature, the large number of classical MD solutions of nanochannel flow are invalid by QM.
To obtain valid MD simulations, standard MD computer algorithms require modification to simulate the QM effect of vanishing heat capacity.
Allen & Tildesley algorithms modified
14

## Slide 15: Model-Method
Points P1 and P2 (blue) are for visual references as the water molecules move back and forth along the X-axis
The L-J parameters for water were,  = 0.315 x10 -9 m and  = 73.3 k.
Frictionless flow simulated by reducing  by a factor of 100.
Initially, all molecules move at velocity V = 1 m/s in the positive X direction.
Each water molecule carries a 1 fs fluctuating charge q = 1 e
The time step t = 0.001 fs
Solutions on a PC took 1.5 million iterations and < 1 minute.
15

## Slide 16: Results
16
Displacement
Velocity
String Length

## Slide 17: Displacement
Chart: 
The X displacement response after the charge Q reacts with charge q of each of the molecules. The molecule nearest point P2 (blue) responds immediately to charge Q. The molecule nearest P1 (yellow) responds later.
17

## Slide 18: Velocity
Chart: 
Velocities < 0 show deceleration.
The molecule nearest P2 (blue) underwent oscillation at 40 GHz
18

## Slide 19: String Length
Chart: 
The string length L is disrupted during deceleration, the minimum occurring during compression with the maximum after repulsion.
19

## Slide 20: Review & Comment
Based on classical MD, the prevailing view that:
(1) Stationary charge outside a nanochannel blocks single-file flow depending on the orientation of the water molecules, and
(2) Vibrating charge increases flow as hydrogen bonds are broken
is inconsequential to the QM charging by X-rays
By QM, all hydrogen bonds broken and atoms charged:
(1) Stationary charge blocks flow by Coulomb repulsion of all atoms, and
(2) Increased flow is caused by the reduced friction from Coulomb repulsion of all atoms and channel wall

## Slide 21: Conclusions
20
MD simulations of 10 water molecules through a CNT were performed with QM that precludes conservation of heat by temperature.
Heat is conserved by producing X-rays that charge the water molecules
Coulomb repulsion produces frictionless flow  Bernoulli equation.
Under high EM confinement, the free electrons recombine with the charged atoms every 1 fs to produce electro-neutrality only to promptly ionize once again, the process repeating until the string of molecules leaves the CNT.
The CNT diameter d < 1 nm is small enough to create X-rays as turbulence brings water molecules having kT energy in the surroundings to the CNT surface to be expended in creating X-rays.
In application to nanopores, the heat flow from the kT energy in the membrane is sufficient to raise the pore to X-ray levels in about 10 fs .
Experiments are needed to verify MD simulations !

## Slide 22: Questions & Papers
Email: nanoqed@gmail.com
http://www.nanoqed.org
21
Notes: Enter speaker notes here.